ARM / Linux
Advanced RISC machine
Worlds most used 32bit architecture
95% of smartphones
Low power, low heat

---
SoC - System on Chip
Marvell, Nvidia, pi, Samsung ...
Smaller, faster, cheaper
Low power, low heat
Marvell once owned by Intel

---
Size

---
Example Block Diagram

---
SoC Boot Sequence
Power on, loads the Boot ROM
Bootrom loads U-Boot from flash (usually)
U-Boot loads Linux (uImage) from wherever
uImage is a kernel with a U-Boot header
NO grub/lilo

---
Q & A
What is U-Boot ? How to make one?
U-Boot is a bootloader in place of GRUB/LILO.
U-Boot is usually in flash memory.
Manufacturers supply the executable.
Good manufacturers supply the source.
There is always the Denx version
http://www.denx.de/wiki/U-Boot/
Simple to set up – demo later.

---
Why won't Ubuntu work with all ARM chips?
Ubuntu is different and is targeted at the corporate desktop.
Ubuntu has a fuzzy distinction between kernel and distro. Rapidly becoming an Intel only distribution.

---
Why are there many different types of ARM chips on the market?
Purpose built SoCs. e.g. Phones, Media Players
ARM design to suit task at hand.
Evolution.

---
What is the difference between ARMv5 v7 v8 v9 and are they faster?
Different chip design. Different instruction set.
Speed is usually more influenced by the SoC (e.g. memory, clock cycles, hardware support).
Is there gcc (compiler) support for ARM v* ?

---
Which distro to pick for PXE boot?
Debian, ArchLinux, Fedora
PXE Boot is performed largely by U-Boot.
Debian and ArchLinux are both small, so less network load.

---
Not all software works on ARM chips, what does and what I can do with it.
Software compiled for Intel will not work on ARM systems.
Recompile.
Almost everything works on ARM, hardware tools excepted.

---
All ARM devices seem to use different graphics chips which I've never heard of before, there doesn't seem to be a standard and some are open source and some are not? Which are the best to get and how can I get drivers installed for the graphics chip so I can play HD content?
This all depends on the SoC in question. Usually the manufacturer supplies binary versions of the required drivers. A few are mainline Linux. Everyone is working hard to get their drivers in mainline Linux.

---
Installation seems different between ARM devices (ie: Raspberry PI you dd an image, CuBox you have to do it through the USB link, Nexus 7 you have to download a special tool on an Ubuntu system & unlock the device). There doesn't seem to be as many standards.
Bad documentation and manufacturers giving bad advice. CuBox, MiraBox, Dreamplug etc can all by rebuilt in minutes using standard Linux tools (e.g. cp)

---
What's in it for Linux
- Every computing device on the planet
- Low power, fanless servers
- Opposite to server virtualization
- Home user familiarity
- Funding